## Slide 2: IP address is an address having information about how to reach a specific host, especially outside the LAN. An IP address is a 32 bit unique address having an address space of 232.

## Slide 3: Note
An IPv4 address is 32 bits long.

## Slide 4: Note
The IPv4 addresses are unique and universal.

## Slide 5: Note
The address space of IPv4 is
232
or 4,294,967,296.

## Slide 7: IPv4 address is divided into two parts Network ID Host ID

## Slide 8: Figure 19.1 Dotted-decimal notation and binary notation for an IPv4 address

## Slide 9: Change the following IPv4 addresses from binary notation to dotted-decimal notation.
Example 19.1
Solution
We replace each group of 8 bits with its equivalent decimal number (see Appendix B) and add dots for separation.
????
????

## Slide 10: Change the following IPv4 addresses from dotted-decimal notation to binary notation.
Example 19.2
Solution
We replace each decimal number with its binary equivalent (see Appendix B).

## Slide 11: Find the error, if any, in the following IPv4 addresses.
Example 19.3

## Slide 12: Note
In classful addressing, the address space is divided into five classes: A, B, C, D, and E.

## Slide 13: Figure 19.2 Finding the classes in binary and dotted-decimal notation

## Slide 14: Find the class of each address.
a. 00000001 00001011 00001011 11101111
b. 11000001 10000011 00011011 11111111
c. 14.23.120.8
d. 252.5.15.111
Example 19.4

## Slide 15: Table 19.1 Number of blocks and block size in classful IPv4 addressing

## Slide 16: Note
In classful addressing, a large part of the available addresses were wasted.

## Slide 17: Table 19.2 Default masks for classful addressing

## Slide 18: Note
Classful addressing, which is almost obsolete, is replaced with classless addressing.

## Slide 19: Figure 19.3 A block of 16 addresses granted to a small organization

## Slide 20: Note
In IPv4 addressing, a block of addresses can be defined as
x.y.z.t /n
in which x.y.z.t defines one of the addresses and the /n defines the mask.

## Slide 21: Note
The first address in the block can be found by setting the rightmost 32 − n bits to 0s.