## Slide 1: Networking Commands
PING
TRACERT
3. show ip route - to check the route of router
4. show mac-address-table - to check the mac table of switch.
5. netstat
6. IPCONFIG
7. nslookup
8.ARP

## Slide 2: PING
PING IS : Packet Internet or Inter-Network Groper is a basic Internet program that allows a user to test and verify if a particular destination IP address exists and can accept requests in computer network administration.
Internet Control Message Protocol (ICMP) is probably most well known as the message protocol used for the ping command. A ping command sends an ICMP echo request to the target host. The target host responds with an echo reply.

## Slide 3
C:\>ping 192.168.25.98
Pinging 192.168.25.98 with 32 bytes of data:
Request timed out.
Request timed out.
Request timed out.
Request timed out.
Ping statistics for 192.168.25.98:
Packets: Sent = 4, Received = 0, Lost = 4 (100% loss),
C:\>ping 192.168.25.98
Pinging 192.168.25.98 with 32 bytes of data:
Reply from 192.168.25.98: bytes=32 time=35ms TTL=125
Reply from 192.168.25.98: bytes=32 time=13ms TTL=125
Reply from 192.168.25.98: bytes=32 time=20ms TTL=125
Reply from 192.168.25.98: bytes=32 time=5ms TTL=125
Ping statistics for 192.168.25.98:
Packets: Sent = 4, Received = 4, Lost = 0 (0% loss),
Approximate round trip times in milli-seconds:
Minimum = 5ms, Maximum = 35ms, Average = 18ms

## Slide 4: TRACERT /TRACE ROUTE
The traceroute command on a Cisco device or in network can be used to identify the path used by a packet to reach its target.
It identifies all the routers in the path from the source host to destination host and it can be useful when troubleshooting network problems.
Using this command you can figure out which router in the path to an unreachable target should be examined more closely as the probable cause of the network’s failure.

## Slide 5: Example
C:\>tracert 192.168.25.98
Tracing route to 192.168.25.98 over a maximum of 30 hops:
1 0 ms 0 ms 3 ms 192.168.25.1
2 1 ms 11 ms 0 ms 192.168.25.102
3 1 ms 13 ms 14 ms 192.168.25.106
4 23 ms 13 ms 12 ms 192.168.25.98
Trace complete.

## Slide 6: ARP(Address Resolution Protocol)
With ARP command it allows to display and modify the Address Resolution Protocol (ARP) cache.
An ARP cache is a simple mapping of IP addresses to MAC addresses.
Each time a computer’s TCP/IP stack uses ARP to determine the Media Access Control (MAC) address for an IP address, it records the mapping in the ARP cache so that future ARP lookups go faster.

## Slide 7
C:\Users>arp
Displays and modifies the IP-to-Physical address translation tables used by
address resolution protocol (ARP).
ARP -s inet_addr eth_addr [if_addr]
ARP -d inet_addr [if_addr]
ARP -a [inet_addr] [-N if_addr] [-v]
-a Displays current ARP entries by interrogating the current
protocol data. If inet_addr is specified, the IP and Physical
addresses for only the specified computer are displayed. If
more than one network interface uses ARP, entries for each ARP
table are displayed.
-g Same as -a.
-v Displays current ARP entries in verbose mode. All invalid
entries and entries on the loop-back interface will be shown.
inet_addr Specifies an internet address.
-N if_addr Displays the ARP entries for the network interface specified
by if_addr.
-d Deletes the host specified by inet_addr. inet_addr may be
wildcarded with * to delete all hosts.
-s Adds the host and associates the Internet address inet_addr
with the Physical address eth_addr. The Physical address is
given as 6 hexadecimal bytes separated by hyphens. The entry
is permanent.
eth_addr Specifies a physical address.
if_addr If present, this specifies the Internet address of the
interface whose address translation table should be modified.
If not present, the first applicable interface will be used.
Example:
> arp -s 157.55.85.212 00-aa-00-62-c6-09 .... Adds a static entry.
> arp -a .... Displays the arp table.

## Slide 8
C:\Users>arp -a
Interface: 172.21.192.134 --- 0x3
Internet Address Physical Address Type
172.21.192.1 54-7c-69-01-e9-52 dynamic
172.21.192.104 e4-d5-3d-78-c2-b0 dynamic
172.21.192.117 68-54-5a-a8-87-b1 dynamic
172.21.192.118 78-0c-b8-62-69-f2 dynamic
172.21.192.126 64-5a-04-61-8c-dc dynamic
172.21.192.131 12-7a-ab-9a-81-81 dynamic
172.21.192.140 94-08-53-3a-00-15 dynamic
172.21.192.149 14-85-7f-06-93-3e dynamic
172.21.192.163 b8-81-98-b6-f7-60 dynamic
172.21.192.168 5c-ea-1d-02-8d-39 dynamic
172.21.192.173 10-60-4b-d9-76-c2 dynamic
172.21.192.181 34-7d-f6-d2-53-20 dynamic
172.21.192.188 64-bc-58-18-5d-8f dynamic
172.21.192.190 80-2b-f9-65-fd-71 dynamic
172.21.192.191 78-e4-00-0c-9b-77 dynamic
172.21.192.193 10-3d-1c-cd-5a-2d dynamic
172.21.192.197 5c-61-99-31-98-61 dynamic
172.21.192.200 70-66-55-a6-0f-bd dynamic
172.21.192.213 dc-a2-66-1e-2c-5f dynamic

## Slide 9: ARP COMMAND IN CISCO PACKET TRACER
C:\>arp
Cisco Packet Tracer PC ARP
Display ARP entries: arp -a
Clear ARP table: arp -d
C:\>arp -a
Internet Address Physical Address Type
192.168.25.2 00d0.9767.a17a dynamic

## Slide 10: NETSTAT
The netstat command, meaning network statistics, is a Command Prompt command used to display very detailed information about how your computer is communicating with other computers or network devices.
Specifically, it can show details about individual network connections, overall and protocol-specific networking statistics, and much more, all of which could help troubleshoot certain kinds of networking issues.

## Slide 11
C:\Users\dell>net stat
Active Connections
Proto Local Address Foreign Address State
TCP 172.21.192.204:51657 a23-215-196-10:https CLOSE_WAIT
TCP 172.21.192.204:51658 117.18.237.29:http CLOSE_WAIT
TCP 172.21.192.204:52055 20.106.94.33:https ESTABLISHED
TCP 172.21.192.204:52118 40.97.120.66:https ESTABLISHED
TCP 172.21.192.204:52119 40.97.120.66:https ESTABLISHED
TCP 172.21.192.204:53637 relay-30fbe9f1:http ESTABLISHED
TCP 172.21.192.204:53646 20.197.71.89:https ESTABLISHED
TCP 172.21.192.204:54191 sf-in-f188:5228 ESTABLISHED
TCP 172.21.192.204:54311 del03s10-in-f3:https TIME_WAIT
TCP 172.21.192.204:54312 10.10.0.1:http TIME_WAIT
TCP 172.21.192.204:54313 10.10.0.1:http TIME_WAIT
TCP 172.21.192.204:54314 a-0001:https ESTABLISHED
TCP 172.21.192.204:54315 13.107.246.254:https ESTABLISHED
TCP 172.21.192.204:54316 13.107.49.254:https ESTABLISHED
TCP 172.21.192.204:54317 13.107.6.254:https ESTABLISHED
TCP 172.21.192.204:54318 204.79.197.222:https ESTABLISHED
C:\Users\dell>

## Slide 12: NSLOOKUP
nslookup command is used for obtaining server records.
Converting a domain name to its IP address using the nslookup command is one of them. One can also find IP address of any website’s host machine.

## Slide 13: Example of nslookup in Cisco Packet Tracer with DnS Server
C:\>nslookup lpu.in
Server: [192.168.25.2]
Address: 192.168.25.2
DNS request timed out.
timeout was 15000 milli seconds.
DNS request timed out.
timeout was 15000 milli seconds.
DNS request timed out.
timeout was 15000 milli seconds.
Server: [192.168.25.2]
Address: 192.168.25.2
Non-authoritative answer:
Name: lpu.in
Address: 192.168.25.2

## Slide 14: Example of nslookup in cmd prompt in windows
C:\Users>nslookup www.lpu.in
Server: UnKnown
Address: 172.19.2.254
Non-authoritative answer:
Name: www.lpu.in
Addresses: 2606:4700:20::681a:ccd
2606:4700:20::681a:dcd
2606:4700:20::ac43:4a98
104.26.12.205
172.67.74.152
104.26.13.205
C:\Users>nslookup google.com
Server: UnKnown
Address: 172.19.2.254
Non-authoritative answer:
Name: google.com
Addresses: 2404:6800:4009:800::200e
142.250.194.238